## Slide 1: Wi-Fi Tracker
Ryan Ly
Donald Taylor
Mohammad Aljagthmi
Jacob Manser

## Slide 2: Overview
Project Goals
Design Approach
Approach of Test Requirements
Summary of Results
Conclusion

## Slide 3: Project Goals
To create an item tracker that connects to a mobile application that will give the user access to the tracker’s location
The tracker can be attached and removed by the user to whatever object the user wants to track
The mobile application will serve as the interface with the user

## Slide 4: Design Approach
To accomplish milestone goals, we split the tasks amongst the group members. This was our “divide-and-conquer” strategy
Ly – Hardware, wiring, physical packaging of the product
Taylor – Database and communication between app and chip
Aljagthmi – GUI and App development
Manser – Hardware programming of the chip

## Slide 5: Design Approach - Ly
Solder pinouts to the Adafruit Huzzah ESP8266 HUZZAH breakout chips. This was necessary for the programming of the chips using the Arduino IDE
Create case/package that holds all necessary parts for function. This includes the chip, battery, RFID tag, and the strap/attachment method
Once the programming of the chip was complete, de-solder and re-solder pinout connections of chips to fit on packaging
(Unexpected) Program chip to connect to a TCP server

## Slide 6: Design Risks - Ly
Highly dependent on parts arriving on time
Soldering experience was necessary for the tasks (had prior experience already)
Lack of communication with Manser. Ly programmed ESP8266 to establish TCP socket connection with server that Taylor made

## Slide 7: Design Approach - Taylor
Developing and integrating the Firebase database
Developing and integrating background services between server and chip
(Unexpected) Designing app layout
(Unexpected) Setting up TCP server
(Unexpected) Helped Ly with programming chip to communicate with TCP server

## Slide 8: Design Risks - Taylor
Android OREO kills long running background services
(Requirement creep) Project and Redpin required a server for constant communication
Integration reliant on having a fully developed application and programmed chip

## Slide 9: Design Approach - Aljagthmi
Graphical user interface application designed to allow user to access and edit data stored in the database. Contains two subsystems:
  Login Operations – controls the user access to the application or registration if no user data is found
  Device Configuration – controls configuration, addition, and display of Tracker information from and to the database for the GUI
Log in page is displayed to user with username and password fields are displayed on the page
Username field should be editable and accept the username
Password field should be editable and accept the password and display as stars or dots
User should log in into application and navigate to Home page
GUI Development

## Slide 10: Design Risks - Aljagthmi
Development
Creation of the mobile application might take longer than anticipated

## Slide 11: Design Approach - Manser
Hold down the GPIO0 and Reset Button for around five seconds to set the Adafruit Huzzah to programmable mode
Start Arduino IDE and open up the Preference window to add the URL http://arduino.esp8266.com/stable/package_esp8266com_index.json in the Additional Board Manager section in order to select the correct board manager (Adafruit HUZZAH 8266)
Program to see if it was possible to make the LED light blink
Program to see if the chip was able to establish a Wi-Fi connection with the local Internet

## Slide 12: Design Risks - Manser
Lots of cross-platforming to ensure compatibility on all devices.
Had to experiment with many Applications to ensure
Application during testing would often bug out, would have to reset the device and application to start programming again.
Lack of experience with the software increased the time of completing many steps.

## Slide 13: Approach to Test Requirements
A spreadsheet was made detailing the requirements and the steps it takes to fulfill them
The spreadsheet detailed a complete user experience navigating through the various features of the app and the tracker

## Slide 14: Summary of Results
Passed Requirements
Req No. | Obj No. | Requirement
1 | 1 | Device shall comply with IEEE 802.11 communication standard
3 | 1 | Device shall communicate with a mobile application
5 | 4 | Device shall contain an attached LED light that conforms to ANSI C82.16-2015 standard
7 | 3 | Mobile application shall be usable on a mobile device running Android 4.4 or newer
10 | 3 | Mobile application shall allow the user to configure an audible tone of at least 60dB for an input date and time
14 | 3 | Mobile application shall store user defined email
16 | 5 | Device shall provide the user access to the battery through a folding panel
17 | 5 | Device shall accept a replacement battery of the same form factor
18 | 6 | Device shall function in temperatures above 32­­­­0F
21 | 6 | Device shall function following a 3 ft exposure to unaccelerated gravity
Failed Requirements
Req No. | Obj No. | Requirement
2 | 1 | Device shall use an open source positioning system over Wi-Fi
4 | 2 | Device shall adhere to surfaces that meet SPI standards A-3, B-1, B-2, B-3, C-1, C-2, C-3 for molded plastic with Velcro© pads
6 | 1 | Device shall include a mobile application
8 | 3 | Mobile application shall email the user provided email address when battery voltage drops below 80% of factory listed voltage
9 | 3 | Mobile application shall allow the user to configure a visual alarm for an input date and time
11 | 3 | Mobile application shall allow the user to configure the LED light to turn on for an input date and time
12 | 3 | Mobile application shall allow the user to see location information for the device
13 | 3 | Mobile application shall allow the user to define a custom name for the device
15 | 3 | Mobile application shall store user defined wi-fi network credentials
19 | 6 | Device shall function in temperatures not exceeding 1500F
20 | 6 | Device shall function if exposed to 8 fl oz of water

## Slide 15: Lessons Learned
Research needed to be deeper. Some things were either overlooked or we did not know we needed them.
Communication is important. Very important. It hurts how important.
Had functional design flow, but needed more visual design flow
Needed more/better validation steps for completing tasks

## Slide 16: What We Should Have Done Differently
Should have divided milestones into more concrete tasks
Should have done application design as a group at the beginning
Should have used online tools such as GitHub and Slack more often and more consistently
Should have bugged each other to get tasked done
A strike did not help
Should have began and consistently worked on chip programming

## Slide 17: Conclusion
Our project had a chance to work
Setbacks include
  Unexpected complexities
  Lack of use of online tools
  Lack of communication
  Lack of concrete design
  Parts not coming in at optimal time
  Lack of solid process to meet milestones